## Slide 1: NIPIN ESD Protection Diode
Project Course - Prof. Sandip Lashkare
By: Krish Patel

## Slide 2: ESD Protection Window
Green: IC Operating
Normal voltage range where IC operates safely
Blue: Safety Margin
Buffer zone before protection device triggers
White: ESD Protection Zone
Voltage range where protection device must clamp safely
Red: Failure Zone
Breakdown of gate oxide or core junction — fatal
Yellow: Second Breakdown
Dangerous regime after the ESD device itself fails

## Slide 3: Device Structure and Concept?
The NIPIN punch-through diode consists of n+-i-p+-i-n+ layers, where the thin p+ region (2-7nm) between two intrinsic (i) regions creates a triangular potential barrier. This design enables punch-through breakdown at ultra-low voltages (<0.5V) and bi-directional operation, making it ideal for ESD protection.
Device Structure

## Slide 4: How is the Breakdown Voltage Reduced to <0.5V ?
In case of a normal diode, impact ionization occurs when a high-energy electron collides with atoms in the crystal lattice, knocking free additional electron-hole pairs. This usually requires energy equal to or greater than the bandgap energy (Eg) of the material (e.g., >1.1 eV for silicon).
However in the case of NIPIN diode, happens sub-bandgap impact ionization
, electrons with less than the bandgap energy still cause ionization. This happens due to:
High electric fields in the ultra-thin region p+ layer .
Hot electrons from the tail of the Boltzmann energy distribution having enough energy to trigger ionization, even at voltages below Eg.

## Slide 5: How is the Capacitance Reduced ?
Intrinsic layers act as spacers, increasing depletion width
Punch-through effect modifies charge distribution(Distributed Charge)
Low doping in the i-region further increases depletion width
Lower parasitic capacitance makes it ideal for high-speed circuits
NIPIN diode is intended for low-voltage, high-speed applications such as USB 3.0, HDMI, Thunderbolt, and RF circuits due to its low capacitance and fast response time

## Slide 6: Electrostatics Of NIPIN Diode
.

## Slide 7: Band Diagram
The band diagram of the NIPIN diode has a shape of triangular barrier region.
Value of Vb0 = 0.32 V, due to this low value of Vb0 this diode can be used for low voltage application.
Through the plot we observe due to the presence of intrinsic region the length of depletion width increases.

## Slide 8: Charge Profile
From the Charge profile Diagram we can say that:
qNdLn + qNdLn = qNaLp
2*NdLn = NaLp
The charge profile shows the similarity with the one derived theoretically.

## Slide 9: Depletion Region and Punch Through
From the charge profile we can observe the presence of the depletion region, in the p region and on the edge of I and N region.
The diode goes through the punch through which we can observe through the complete depletion of I and P region.

## Slide 10: Electric Field
Through, charge profile we can derive the electric field profile:
E_max = 1/ε q Nd Ln= (qNa Lp)/2ε
The Electric field profile of the Nipin diode shows similarity with the theoretically plotted graph.
Here the p region is under full depletion due to which there is a continuous drop in the value.

## Slide 11: Electric Potential
The plot shows a symmetric potential drop in the middle, with a potential barrier Vb0.
Therefore, the value of 𝑉𝑏0 is equal to the are under the first trapezium in electric field profile.
𝑉𝑏0 = 1/2[𝐿𝑛+𝐿𝑖+𝐿𝑝/2+𝐿𝑖]𝐸𝑚𝑎𝑥
= (𝑞𝑁𝑑 𝐿𝑛2)/2𝜀 + (𝑞𝑁𝑎 𝐿𝑖 𝐿p)/2𝜀 + (𝑞𝐿𝑝2 𝑁𝑎)/8𝜀
Since, 𝐿𝑛 and 𝐿𝑝 have low magnitude so there square value will be negligible.
𝑉𝑏0 =(𝒒𝑵𝒂 𝑳𝒊 𝑳𝒑)/𝟐𝜺

## Slide 12: Plots Analysis

## Slide 13: TLP Plot of Standard Values
Rdyn is the Resistance experienced by the shunted current , Lesser Rdyn indicates Better Protection as More Current is shunted resulting in lesser current flow to the DUP
Clamping Voltage (Vₛ) is the maximum voltage a Transient Voltage Suppression (TVS) diode or ESD protection device allows across a circuit before it starts conducting heavily to divert excess transient energy

## Slide 14: Vb0with Lpand Na variance
Formula for Vb0=
qNaLiLp/2ε
We can observe that the value of Vb0as we increase the value of Li since it is proportional to Vb0.
The value of Vb0 increase linearly initial for all value of Lp but it begins to saturate for higher values of Lp.

## Slide 15: Vb0 with Na and Li variance
Formula for Vb0= qNaLiLp/2ε
We can observe that the value of Vb0 as we increase the value of Li since it is proportional to Vb0.
It shows that the value of Vb0 is directly proportional to Na, Li and Lp.

## Slide 16: Lᵢ Variation
As Li increases Barrier Height Increases due to which the Vbr of the diode increases
With a very long i-region (>50nm), the voltage needed for breakdown increases significantly.

## Slide 17: Semilog Scale
A shorter i-region reduces the depletion region size, making it easier for electrons to tunnel through.
This increases leakage current, which is undesirable in ESD protection.

## Slide 18: Nₐ Variation
If p+ doping is low, the barrier height is low, allowing more electrons to tunnel through thus a Low Vbr also it results in more leakage current.
Increasing p+ doping concentration increases breakdown voltage.
Inference: A high enough p+ doping (≈10¹⁹ cm⁻³) is needed to maintain a strong barrier while preventing excessive leakage.

## Slide 19: Lₚ⁺ Variation
Increasing Lₚ⁺ increases the barrier height due to which the Vbr increases,
A shorter p+ region creates a sharper, triangular potential barrier, which helps with impact ionization at low voltages.
However, too high Lₚ⁺ flattens the triangular barrier, making the impact ionisation less effective even though it increases Breakdown Voltage.

## Slide 20: DC IV Curve
The NIPIN DC-IV curve shows a sharp drop in current near 0V because the middle Intrinsic (I) layer creates a wide depletion region, restricting charge carrier movement. This depletion region causes very low current flow at small voltages
As voltage increases, the current rises since charges get enough energy to move.
The curve is symmetric because the structure is balanced on both sides.

## Slide 21: Doping Conc. @1000K
The red regions at both ends indicate highly doped n-type regions, ensuring strong conductivity with abundant charge carriers.
The green region in the middle represents intrinsic Layers or lightly doped area.
The doping profile is symmetrical, indicating a well-balanced structure, which helps in maintaining uniform electric field distribution
Doping in Right Corner
Doping in left corner

## Slide 22: Electric Field @ 1000K
The electric field strength decreases as X increases, meaning the force acting on charge carriers weakens over distance.
The strongest field appears in a small hotspot near the center, likely at the junctions, where charge separation is most intense, aiding fast carrier movement.
At the edge of N-I, the electric field is strong because of the depletion region due to bond charges.
As we go towards P region the potential value decreases.

## Slide 23: Potential @1000K
The gradual transition from high potential (red) to low potential (blue) indicates a well-defined built-in electric field,
The central region (green) corresponds to the intrinsic (i) layer, where the potential is more evenly distributed, ensuring minimal carrier recombination

## Slide 24: Is Current Density High Where Impact Ionization is High?
Impact ionization generates additional electron-hole pairs, increasing the carrier concentration (n) in the semiconductor. Since current density (J) is directly proportional to carrier concentration, higher impact ionization leads to a higher current density in that region.

## Slide 25: Lattice @1000K
In the case of lattice temperature the value increases in the region of High current density and impact ionization.
This trend shows us a direct relation between temperature and impact ionization, which leads towards higher current density.

## Slide 26: Asymmetric Structure
.

## Slide 27: Structural overview and electrical behavior of the asymmetric NIPIN diode
Asymmetrical Design: Li-1, Li-2 regions with p⁺ center enable punch-through.
Capacitance Model: C_eff ≈ C2 in asymmetric case (C1 ≫ C2).
IV Trends: Higher Li-2 lowers forward current and delays breakdown.
Band Diagram: Increasing Li-2 flattens barrier, reducing electric field.

## Slide 28: Lᵢ Variation
As Li increases Barrier Height Increases due to which the Vbr of the diode increases

## Slide 29: TEMP-Lᵢ Variation
TLP curves for different Li-2 values, showing a shift in breakdown voltage and increase in the temperature with increasing intrinsic length.

## Slide 30: Capacitance Variation
Capacitance decreases consistently with increasing Li-2, while lower Li-1 values exhibit higher overall capacitance.

## Slide 31: Conclusion
The plot shows simulated IV and Temp-V characteristics for the diode with Li-1 = 20nm and Li-2 = 50nm. The structure demonstrates sub-bandgap breakdown near 0.7V with a peak current of 2.2mA/µm at 1000K. The extracted junction capacitance is 1.49pF/mm^2